## Slide 1: Computer Organization and Design Instruction Sets 2
Henry Fuchs
Slides adapted from previous instructors of this class: Montek Singh, Anselmo Lastra, Leonard McMillan and from Gary Bishop
Back to McMillan & Chris Terman, MIT 6.004 1999
Monday, Sept. 16 and Friday, Sept. 20, 2019
Lecture 5

## Slide 2: Today
More instructions
  signed vs. unsigned instructions
  larger constants
  accessing memory
  branches and jumps
  multiply, divide
  comparisons
  logical instructions
Reading
  Book Chapter 2.1-2.7
  Study the inside green flap (“Green Card”)

## Slide 3: Recap: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  up to three 5-bit OPERAND fields
    each specifies a register (one of 32) as source/destination
  embedded constants
    also called “literals” or “immediates”
    16-bits, 5-bits or 26-bits long
    sometimes treated as signed values, sometimes unsigned
There are three basic instruction formats:
R-type, 3 register operands (2 sources, destination)
I-type, 2 register operands, 16-bit constant
OP
rs
rt
rd
OP
rs
rt
16-bit constant
func
shamt
J-type, no register operands, 26-bit constant
OP
26-bit constant

## Slide 4: Working with Constants
Immediate instructions allow constants to be specified within the instruction
  Examples
    add 2000 to register $5
    addi $5, $5, 2000
    subtract 60 from register $5
    addi $5, $5, -60
      … no subi instruction!
    logically AND $5 with 0x8723 and put the result in $7
    andi $7, $5, 0x8723
    put the number 1234 in $10
    addi $10, $0, 1234
  But…
    these constants are limited to 16 bits only!
      Range is [-32768…32767] if signed, or [0…65535] if unsigned

## Slide 5: Recap: ADDI
addi instruction: adds register contents, signed-constant:
Symbolic version: addi $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x08, dictating addi
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sxt(imm)
constant field, indicating -3 as second operand
(sign-extended!)
addi rt, rs, imm:
0
0
1
0
0
0
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:

## Slide 6: Beware ADDIU: “add immediate unsigned”
addiu: supposedly “add immediate unsigned”
BUT IS A MISNOMER! Actually sign-extends
the immediate.
Symbolic version: addiu $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x09, dictating addiu
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sign-ext(imm)
constant field, indicating -3 as second operand
(sign-extended!)
addiu rt, rs, imm:
0
0
1
0
0
1
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:
The only difference between addi and addiu is that addiu doesn’t check for overflow. (It still sign-extends!)

## Slide 7: ORI: Unsigned Constants
ori instruction: bitwise OR’s register to unsigned-constant:
Symbolic version: ori $9, $11, 65533
“OR the contents of rs to const; store result in rt”
OP = 0x0d, dictating ori
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] | zero-ext(imm)
Also: All logical operations are always “unsigned”, so always zero-extended:
ori, andi, xori
constant field, indicating 65533 as second operand
(zero-extended!)
ori rt, rs, imm:
0
0
1
1
0
1
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:
The imm is 0-padded into a 32-bit unsigned (+ve) number:
00000000000000001111111111111101

## Slide 8: How About Larger Constants 1 of 4 ?
Problem: How do we work with bigger constants?
  Example: Put the 32-bit value 0x5678ABCD in $5
  CLASS: How will you do it?
One Solution:
  put the upper half (0x5678) into $5
  then shift it left by 16 positions (0x5678 0000)
  now “add” the lower half to it (0x5678 0000 + 0xABCD)
  addi $5, $0, 0x5678
  sll $5, $5, 16
  addi $5, $5, 0xABCD
One minor problem with this:
  2nd addi can mess up by treating the constants are signed
  see next slide

## Slide 9: How About Larger Constants 2 of 4?
So, what’s wrong with this?
  addi $5, $0, 0x5678
  sll $5, $5, 16
  addi $5, $5, 0xABCD
To avoid this problem:
  use ori instead of the second addi
0101011001110111
1010101111001101
1111111111111111
1010101111001101
addi
0101011001111000
0000000000000000
addi
0101011001111000
0000000000000000
sll
sign extension!
0x 5 6 7 7
A B C D
in hex
instead of 0x5678ABCD

## Slide 10: How About Larger Constants 3 of 4 ?
Observation: This sequence is very common!
  so, a special instruction was introduced to make it shorter
  the first two (addi + sll) combo is performed by
  lui
  “load upper immediate”
    puts the 16-bit immediate into the upper half of a register
  Example: Put the 32-bit value 0x5678ABCD in $5
  lui $5, 0x5678
  ori $5, $5, 0xABCD

## Slide 11: How About Larger Constants 4 of 4?
Look at this in more detail:
  “load upper immediate” lui $5, 0x5678 // 0101 0110 0111 1000 in binary
Then must get the lower order bits right
  ori $5, $5, 0xABCD // 1010 1011 1100 1101
0101011001111000
0000000000000000
0000000000000000
1010101111001101
0101011001111000
1010101111001101
ori
0101011001111000
0000000000000000
Reminder: In MIPS, Logical Immediate instructions (ANDI, ORI, XORI) do not sign-extend their constant operand

## Slide 12: Accessing Memory
MIPS is a “load-store” architecture
  all operands for ALU instructions are in registers or immediate
  cannot directly add values residing in memory
    must first bring values into registers from memory (called LOAD)
    must store result of computation back into memory (called STORE)
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
address
address
Central Processing Unit (CPU)

## Slide 13: MIPS Load Instruction
Load instruction is I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is looked up
    value found at this address in memory is brought in and stored in register $rt
lw rt, imm(rs)
Meaning: Reg[rt]= Mem[Reg[rs] + sign-ext(imm)]
Abbreviation: lw rt,imm for lw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:

## Slide 14: MIPS Load Instruction
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is looked up
    value found at this address in memory is brought in and stored in register $rt
lw rt, imm(rs)
Meaning: Reg[rt]= Mem[Reg[rs] + sign-ext(imm)]
Abbreviation: lw rt,imm for lw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:
Control Unit
Data
Path
registers
MEMORY
control
status
instr
data
address
address

## Slide 15: MIPS Store Instruction
Store instruction is also I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is accessed
    reads the value from register $rt and writes it into the memory at the address computed
sw rt, imm(rs)
Meaning: Mem[Reg[rs] + sign-ext(imm)] = Reg[rt]
Abbreviation: sw rt,imm for sw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:

## Slide 16: MIPS Store Instruction
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is accessed
    reads the value from register $rt and writes it into the memory at the address computed
sw rt, imm(rs)
Meaning: Mem[Reg[rs] + sign-ext(imm)] = Reg[rt]
Abbreviation: sw rt,imm for sw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:
Control Unit
Data
Path
registers
MEMORY
control
status
instr
data
address
address

## Slide 17: MIPS Memory Addresses
lw and sw read whole 32-bit words
  so, addresses computed must be multiples of 4
    Reg[rs] + sign-ext(imm) must end in “00” in binary
  otherwise: runtime exception
There are also byte-sized flavors of these instructions
  lb (load byte)
  sb (store byte)
    work the same way, but their addresses do not have to be multiples of 4

## Slide 18: Storage Conventions
• Data and Variables are stored in memory
• Operations done on registers
• Registers hold Temporary results
1000:
1004:
1008:
1010:
100C:
n
r
x
y
Addr assigned at compile time
int x, y;
y = x + 37;
x=0x1008
y=0x100C
lw $t0, x($0)
addiu $t0, $t0, 37
sw $t0, y
or, more
humanely,
to
rs defaults to Reg[0] (0)
lw $t0, 0x1008($0)
addiu $t0, $t0, 37
sw $t0, 0x100C($0)
translates
to
Compilation approach:
LOAD, COMPUTE, STORE

## Slide 19: MIPS Branch Instructions
if (REG[RS] != REG[RT])
{ PC = PC + 4 + 4*offset; }
bne rs, rt, label # Branch if not equal
if (REG[RS] == REG[RT])
{ PC = PC + 4 + 4*offset; }
beq rs, rt, label # Branch if equal
NB: Branch targets are specified relative to the next instruction (which would be fetched by default). The assembler hides the calculation of these offset values from the user, by allowing them to specify a target address (usually a label) and it does the job of computing the offset’s value. The size of the constant field (16-bits) limits the range of branches.
OPCODE
rs
rt
16-bit signed constant
MIPS branch instructions provide a way of conditionally changing the PC to some nearby location...
I-type:
Notice on memory references offsets are multiplied by 4, so that branch targets are restricted to word boundaries.

## Slide 20: MIPS Jumps
The range of MIPS branch instructions is limited to approximately  32K instructions ( 128K bytes) from the branch instruction.
To branch farther: an unconditional jump instruction is used.
Instructions:
  j label # jump to label (PC = PC[31-28] || CONST[25:0]*4)
  jal label # jump to label and store PC+4 in $31
  jr $t0 # jump to address specified by register’s contents
  jalr $t0, $ra # jump to address specified by first register’s contents and store PC+4 in second register
Formats:
J-type: used for j
OP = 2
26-bit constant
J-type: used for jal
OP = 3
26-bit constant
R-type, used for jr
OP = 0
rs
func = 8
0
0
0
R-type, used for jalr
OP = 0
rs
func = 9
0
0
rd

## Slide 21: Examples of j and jal
Suppose PC is currently 0x00000004; $8=0x00001234
Suppose PC is currently 0x56780000
  remember: leftmost 4 bits (or 1 hexit) are “sticky”
instr: | new PC value |  | $31 changed?
j 0x4 | 0x4 * 4 = 16 | 0x00000010 | 
j 0x20 | 0x20 * 4 | 0x00000080 | 
jal 0x20 | 0x20 * 4 | 0x00000080 | 0x00000008
jalr $8,$31 | $8 | 0x00001234 | 0x00000008
instr: | new PC value |  | $31 changed?
j 0x20 | 0x {5, 0000080} | 0x50000080 | 
jal 0x20 | 0x {5, 0000080} | 0x50000080 | 0x56780004
jr $31 | value of $31 | 0x56780004 | 

## Slide 22: Multiply and Divide
Slightly more complicated than add/subtract
  multiply: product is twice as long!
    if A, B are 32-bit long, A * B is how many bits?
  divide: dividing integer A by B gives two results!
    quotient and remainder
Solution: two new special-purpose registers
  “Hi” and “Lo”

## Slide 23: Multiply
MULT instruction
  mult rs, rt
  Meaning: multiply contents of registers $rs and $rt, and store the (64-bit result) in the pair of special registers {hi, lo}
    hi:lo = $rs * $rt
  upper 32 bits go into hi, lower 32 bits go into lo
To access result, use two new instructions
  mfhi: move from hi
    mfhi rd
      move the 32-bit half result from hi to $rd
  mflo: move from lo
    mflo rd
      move the 32-bit half result from lo to $rd

## Slide 24: Divide
DIV instruction
  div rs, rt
  Meaning: divide contents of register $rs by $rt, and store the quotient in lo, and remainder in hi
    lo = $rs / $rt
    hi = $rs % $rt
To access result, use mfhi and mflo
NOTE: There are also unsigned versions
  multu
  divu

## Slide 25: Now we can do a real program: Factorial...
Factorial iteratively in C:
  input is in n
    assume constant value of 11
  output will be in ans
  two “temps” used: r1, r2
  assume n is small
    n! will fit within an int
int n=11;
int ans, r1, r2;
r1 = 1;
r2 = n;
while (r2 != 0) {
r1 = r1 * r2;
r2 = r2 – 1; }
ans = r1;
Note:
  the use of r1 and r2 may seem unnecessary
    you can write code just using n and ans
  they are introduced to better relate to the assembly code that results from this C program

## Slide 26: Factorial in assembly
variables are in memory, e.g.:
  n  mem addr 0x1000
  ans  mem addr 0x1004
temps are in registers, e.g.:
  r1  $1, and r2  $2
assume n is small
  n! will fit within a register
int n=11;
int ans, r1, r2;
r1 = 1;
r2 = n;
while (r2 != 0) {
r1 = r1 * r2;
r2 = r2 – 1; }
ans = r1;
n: .word 11 # suppose mem loc 0x1000
ans: .word 0 # suppose mem loc 0x1004
...
addi $1, $0, 1 # $1 = 1
lw $2, 0x1000($0) # $2 = n
loop: beq $2, $0, done # while ($2 != 0)
mult $1, $2 # hi:lo = $1 * $2
mflo $1 # $1 = lo ($1*$2)
addi $2, $2, -1 # $2 = $2 - 1
j loop # loop back
done: sw $1, 0x1004($0) # ans = $1
C code:

## Slide 27: Comparison: slt, slti
slt = set-if-less-than
  slt rd, rs, rt
  $rd = ($rs < $rt) // “1” if true and “0” if false
slti = set-if-less-than-immediate
  slt rt, rs, imm
  $rt = ($rs < sign-ext(imm))
also unsigned flavors
  sltu
  sltiu

## Slide 28: Logical Instructions
Boolean operations: bitwise on all 32 bits
  AND, OR, NOR, XOR
  and, andi
  or, ori
  nor
  xor, xori
Examples:
  and $1, $2, $3
  $1 = $2 & $3
  xori $1, $2, 0xFF12
  $1 = $2 ^ 0x0000FF12
  See all in textbook!

## Slide 29: Logical Instructions
What do these logical operations do?
  ANDing is useful for “masking” off groups of bits.
    ex. 10101110 & 00001111 = 00001110 (mask selects last 4 bits)
  ANDing is also useful for “clearing” groups of bits.
    ex. 10101110 & 00001111 = 00001110 (0’s clear first 4 bits)
  ORing is useful for “setting” groups of bits.
    ex. 10101110 | 00001111 = 10101111 (1’s set last 4 bits)
  XORing is useful for “complementing” groups of bits.
    ex. 10101110 ^ 00001111 = 10100001 (1’s invert last 4 bits)
  NORing is useful for.. uhm…
    ex. 10101110 # 00001111 = 01010000 (0’s invert, 1’s clear)

## Slide 30: Summary – 1 (MIPS memories)
Name | Example | Comments
32 registers | $s0-$s7, $t0-$t9, $zero, $a0-$a3, $v0-$v1, $gp, $fp, $sp, $ra, $at | Fast storage for data, used for arithmetic and logical. $zero always equals zero. Register $at is reserved for the assembler
230 memory words | Memory[0], Memory[4], … Memory[4294967292] | Accessed by data transfer instructions. MIPS uses byte addresses, so sequential words differ by 4. Memory holds data structures, such as arrays, and holds spilled (saved) registers, such as used by procedure calls.

## Slide 31: Summary - 2

## Slide 32: MIPS Instruction Decoding Ring
Top table summarizes opcodes
Bottom table summarizes func field if opcode is 000000
OP | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | func |  | j | jal | beq | bne |  | 
001 | addi | addiu | slti | sltiu | andi | ori | xori | lui
010 |  |  |  |  |  |  |  | 
011 |  |  |  |  |  |  |  | 
100 |  |  |  | lw |  |  |  | 
101 |  |  |  | sw |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 
func | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | sll |  | srl | sra | sllv |  | srlv | srav
001 | jr | jalr |  |  |  |  |  | 
010 |  |  |  |  |  |  |  | 
011 | mult | multu | div | divu |  |  |  | 
100 | add | addu | sub | subu | and | or | xor | nor
101 |  |  | slt | sltu |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 

## Slide 33: Summary
We will use a subset of MIPS instruction set in this class
  Sometimes called “miniMIPS”
  All instructions are 32-bit
  3 basic instruction formats
    R-type - Mostly 2 source and 1 destination register
    I-type - 1-source, a small (16-bit) constant, and a destination register
    J-type - A large (26-bit) constant used for jumps
  Load/Store architecture
  31 general purpose registers, one hardwired to 0, and, by convention, several are used for specific purposes.
ISA design requires tradeoffs, usually based on
  History, Art, Engineering
  Benchmark results